## Slide 1: How to specify the right outreach vehicle
Barbara Battles, SBPL and Michael Swendrowski, SVS
Notes: Introduce self and Michael – working together on new vehicle

## Slide 2: Why put your library through this process?
First things first – get your ducks in a row.
Who are the decision makers?
Who are your customers?
Who are your partners?
Who will provide the funding
What are your goals for the service?
Notes: Things you need to determine first that will affect every decision you make. Keep in mind throughout.

## Slide 3: Identify your decision Makers
The Team
Administration
Outreach Staff
Library Trustees or other governing body
Township Council or Local Government
Other Library Staff Members
Friends, Foundation or other library groups
“The Public”

## Slide 4: Priorities
This is somewhat of a “What came first, the chicken or the egg?” kind of dilemma.

## Slide 5: When to seek help?
Preliminary Planning
Needs assessment
Planning and Conceptual Design
Budgeting and Estimating
Design Development and Documentation
Technical Specification writing
Scheduling and task management
Bid solicitation, analysis and recommendation
Contract negotiation
Implementation and Vendor/Client Liaison
Overall Supervision and Administration
Construction Management
Inspection and Testing
Operator Training

## Slide 6: How will it be purchased and who will own it?
Considerations:
Public Money or Private Money – Individual and/or Corporate
Lease or Own
New or Used
Foundations and grants
Environmental and Fuel Incentives
Grassroots and Crowdsourcing

## Slide 7: Service history and Goals
New Start-up Service
Who suggested this service?
Who will benefit from this service?
How much do you need to do and for how long?
Will you be able to grow or expand once you get started?
Continued Service
Do you want to continue in the same direction?
What has worked and what can be improved, changed or eliminated?
Has the scale of the operation changed over time and will that continue?
Expanded or Additional Services
Where is the current service falling short or is it?
What more could you do?
What do you need to accomplish new goals?

## Slide 8: Information Gathering

## Slide 9: Demographics
What are the characteristics of your target audience?
  Ages
  Education
  Ethnicities and languages spoken
  Location - present and future customers
  Needed and Beneficial Services and materials
  Disabilities and special needs accommodation

## Slide 10: Partnerships

## Slide 11: Community Needs
Basic Library services and materials
Literacy Support
Home Delivery
Institutional Delivery
Accessibility

## Slide 12: Library needs
Outreach
Expansion – Branch vs. Bookmobile
Marketing – more visibility and good will
Educational Support
Additional Service Opportunities

## Slide 13: Scope
Single vehicle
Multiple vehicles (at outset or over time)
Single-use vs Multipurpose Vehicles
Convertible Vehicles

## Slide 14: Staffing and operations
Full-time or part time staff – in house or new-hire
Job Titles and Descriptions
Hours and Days of Operation
Experience and Training
Garaging or staging of vehicle
Maintenance of vehicle
Fuel decisions

## Slide 15: Collection Management
Requirements
Flexibility
Size and Scope
Home location, shifting and loading
Budget and Processing

## Slide 16: Design Considerations
Number of staff and number of seats and workstations
Comfort needs
Layout and Configuration for function
Shelving
Materials
Graphics
Electronics
Display and Storage

## Slide 17: Vehicle Types
Book-bikes, book-boats and other specialty vehicles
Small electronic three-wheeled vehicles
Sprinter vans and smaller delivery vehicles
Trailers
Small RVs
Step Vans
Busses
Trucks
Other

## Slide 18: Small human and electric Powered fair-weather vehicles

## Slide 19: Bikes and Boats

## Slide 20: Vans, Small and mid-sized Delivery Vehicles

## Slide 21: Truck pulled trailers

## Slide 22: Step Vans

## Slide 23: Busses

## Slide 24: Trucks

## Slide 25: Enjoy your vehicle however you use it!

## Slide 26: FURTHER DOWN THE ROAD WITH VEHICLES. 

## Slide 27: Michael swendrowski
33-year veteran of specialty vehicle industry (1986)
Over 1000 vehicles to date
President Specialty Vehicle Services, LLC. (2002)
Chairman ALA Subcommittee on Bookmobiles (2006)
ABOS Board of Directors (2010)
Chair of BOIR Subcommittee
Co-author of On the Road with Outreach (Libraries Unlimited, 2009)
Assisted over 100 libraries with outreach vehicle projects worldwide
Notes: 33-year veteran of specialty vehicle industry (1986)
Over 1000 vehicles to date
  Planters Nut Mobile
  Starbucks Venti Vans
  Lockhead Magic Schoolbus
  OverDrive Digital Bookmobile 1.0 and 2.0
President Specialty Vehicle Services, LLC. (2002)
Chairman ALA Subcommittee on Bookmobiles (2006)
ABOS Board of Directors (2010)
Co-author of On the Road with Outreach (Libraries Unlimited, 2009)
Assisted over 100 libraries with bookmobile projects worldwide

## Slide 28: Base vehicles
Notes: Barbara went over a host of different base vehicle types. I would like to speak a bit further about the most popular choices used for outreach services. 

## Slide 29: Overview
 |  | Overall Length | Overall Width | Floor Height | Interior Height | Collection Capacity | Service Duty | Service Life | Service Types | Base Cost (2018) | Maint. Costs
Truck |  | 28' - 40' | 102" | 32" - 44" | 84" & 91" | 2500 - 6000 | Medium - Heavy | 14-20 years | C, D, E, I, L, LV, P, R, S, U | $225K | Low
Bus |  | 28' - 40' | 96" | 38" - 44" | 77" - 87" | 3500 - 5000 | Heavy | 15-21 years | C, LV, P, R, S, U | $250K | Low
Van |  | 20' - 25' | 78" | 29" - 32" | 66" - 78" | 1000 - 2500 | Light | 7-10 years | C, D, E, H, L, LV, P, S, U | $150K | Low
Cutaway |  | 20' - 26' | 96" | 30" - 36" | 69" - 84" | 1000 - 2000 | Light | 7-10 years | C, D, E, H, I, L, LV, P, S, U | $150K | Medium
Step Van |  | 20' - 40' | 96" | 36" - 42" | 72" - 84" | 1000 - 6000 | Light - Medium | 12-16 years | C, D, I, L, LV, P, S, U | $190K | Medium
Low Floor |  | 28' - 32' | 96" | 12" - 16" | 77" - 84" | 2000 - 3000 | Medium | 9-15 years | C, D, E, H, L, S, U | $250K | High
Service Type Key: |  |  |  |  |  |  |  |  |  |  | 
C = Children Bookmobile |  | H = Homebound Delivery |  |  | LV = Learning Vehicle |  | S = Suburban Bookmobile |  |  |  | 
D = Deposit Collections |  | I - Interlibrary Delivery |  |  | P = Programming |  | U = Urban Bookmobile |  |  |  | 
E = Elderly Bookmobile |  | L = Lobby Stops |  |  | R = Rural Bookmobile |  |  |  |  |  | 
Notes: Refer to chart. General guidelines and data to help.
Length equates to capacity and maneuverability -
REGARDLESS OF WHAT YOU’VE SAID OR HEARD… SIZE DOES MATTER! (share size stories – not enough based on licensing constraints – too much for garage)

## Slide 30: Vans
Low cost
Easy to drive
Highly maneuverable
Limited space
Light service duty
Small collection
Pros
Cons
Notes: Start at about $150K
Very “car like” with AC, power windows & locks, cruise, etc. Even air bags!
Short wheelbase gets in and out of tight spaces.
Limited width (78”) and interior height (78”)
7-10 year life span
Maximum 2,500 volume capacity

## Slide 31: Vans

## Slide 32: cutaways
Cost effective
Rectangular body
High headroom
Light service duty
Minimal weight capacity
Limited length
Pros
Cons
Notes: Not much more than the van
Body is rectangular (more efficient)
More width and height in body
Still have light service duty (more so than van)
Less payload due to heavier body
Only 2 or 3 length options

## Slide 33: cutaways
Notes: With or without walk-through (also a “crawl through” option)
Well suited to programming and learning initiatives (lightweight).

## Slide 34: Step Vans
Aluminum body
Rectangular shape
Multiple lengths
Medium service duty
Utilitarian cockpit
Higher floor
Pros
Cons
Notes: Also known as bread trucks, walk-in vans and UPS trucks
Aluminum body (like truck) lighter weight and doesn’t rust
Rectangular shape is very efficient for shelving (ext. sidewalls great for ext. components… puppet stages, pass-throughs, etc.)
20’ to 40’ on 2’ increments
Not as heavy-duty as truck or bus (designed as delivery vehicle)
Seats uncomfortable and dash is basic.
Relatively high floor (like bus)

## Slide 35: Step Vans

## Slide 36: busses
Very heavy-duty
Rear FMVSS seating
Very maneuverable
Steel body
Curved sidewalls
Low headroom
Pros
Cons
Notes: Heavy-duty, built like a tank to protect our children in a roll-over (high GVWR necessary due to weight)
Can add rear seatbelts
Shorter wheelbase equals tighter turns (sitting in front of steer axle!) 28’ units so maneuverable that they can “porpoise”!
Steel body heavy and prone to rust
Curved sidewalls shrink center aisle and limit shelving height
Only 77” without “roof raise”

## Slide 37: busses
Notes: Front or rear engine placement
Efficient front end (with front engine)

## Slide 38: trucks
Multiple configurations
Ease of use & service
Light & efficient body
Cab is single purpose
No rear FMVSS seating
Wider turn radius
Pros
Cons
Notes: Multitude of options for length, height, engine, and door placements.
“Car like” driving features and hood for engine service.
Aluminum body with rectangular sidewalls. No wheel wells in some!
Loose efficiency of stacking driver/pass over engine
Can’t install rear seatbelts
Longer wheelbase equals wider turns

## Slide 39: trucks
Notes: With or without walk-through.
Very wide aisle (better with aluminum shelving).
Low profile wheels/tires improve floor height.
Lack of wheel wells greatly improves modularity

## Slide 40: Design considerations
Notes: Barbara went over some general considerations. I would like to speak a bit deeper about some popular choices I see daily. 

## Slide 41: Aluminum shelving
Extremely modular
Light weight
Wider aisle
Higher cost
“Non-traditional” look
Less noise attenuation
Pros
Cons
Notes: All connect to the vertical uprights. DVD shelves, divided shelves, desk surfaces, bench seats, etc.
Saves average of 700lbs over wood
Less structure equals wider aisle (42” in Sprinter, 62” in a wood bus, 76” in a 102” wide truck body) 14” more! Show 42”, 62”, 76” string!
Aluminum as a commodity has gotten more expensive
Hard to beat the traditional wood shelving
Doesn’t absorb sound quite as well

## Slide 42: Hybrid power systems
Large battery bank
Additional components
User training
Pros
Cons
Minimize generator use
Stable & quiet power
Eco-friendly
Notes: Use the generator only for necessities, battery charging and backup
Clean and quiet true sine wave power without the need for UPS systems
Less diesel fumes and noise
Large bank because batteries become the primary energy storage
Extra equipment can equal extra headaches down the road
Some additional training is required

## Slide 43: Hybrid power systems
Batteries
Inverter
120V Panel
Transfer Switch
Generator
Shore
Solar Panels
Engine
Computers
LED Lights
USB Receptacles
Diesel Heater
Monitors
Fans
Wheelchair Lift
WiFi
People Counters
Wand
RFID Pad
Printers
Self Check-out
Air Conditioners
AGS
Notes: Basic system powers all loads
Hybrid introduces larger battery bank and inverter… splitting loads into 3 groups (2 powered by batteries). Notice the heater is off the batteries (more in a few)!
Batteries are charged by inverter and engine
Solar can be added to improve run time
Automatic Generator Start (AGS) system can be added to add convenience and reduce user errors

## Slide 44: Lithium-ion power systems
Cost
User training
Pros
Cons
No generator at all!
Stable & quiet power
Eco-friendly
Notes: Next generation in power systems. Automotive grade energy systems designed for vehicle lifetime!
Power large electrical loads with no generator
Designed for solid performance
No noise or fumes
Costs still a bit high
Different way of power thinking

## Slide 45: Lithium-ion power systems
Notes: I thought this 2 minute video may be helpful.
I have visited the Volta plant and feel these products are the future of specialty vehicle power systems!

## Slide 46: Solar panels
Free power
Very low maintenance
Eco-friendly
Initial cost
Not as useful if garaged
Cons
Pros
Notes: Once installed, it’s free (and constant) power
Wipe them off once a year!
Can’t get better than collecting sunshine!
Cost is roughly $1,000 to $1,500 per panel
Fluorescent lighting doesn’t work!

## Slide 47: Diesel- fired heaters
Minimize generator use
Forced air heat
Pre-heating of interior
Initial cost
Cons
Pros
Notes: Is anyone familiar with a diesel fired heater is?
Powered by batteries
Forced air, ducted system (no hot grills to burn ankles)
Can pre-heat interior cabin (thermostatically controlled)
So far… Cost is a bit higher, but elimination of the generator issue must be factored.

## Slide 48: Ruggedized modems
Built-in w/ ext. antennas
VPN and GPS
Also WiFi hotspot
Initial cost
Future replacements
Configuration required
Pros
Cons
Notes: These are built in components (think aircard on steroids!). Bandwidth for 10-20 simultaneous users. Exterior high-gain antennas greatly improve service coverage and bandwidth
Virtual Private Network and GPS tracking available
Cast a WiFi cloud for patron devices.
Cost is about $1200/ea installed
May need replacement as technologies change
There is some configuration necessary from IT dept.

## Slide 49: monitors
Information display
Valuable content
Patron familiarity
Initial cost
Future replacements
Configuration required
Pros
Cons
Notes: Monitors are everywhere we look these days. There is a natural extension in outreach vehicles!
Information display with local or streaming sources
Content can be messaging, entertainment or gaming
Familiar throughout fixed library environments
Always a cost
Technologies age relatively fast
IT folks need to finalize configuration upon delivery

## Slide 50: Video surveillance systems
Staff security
Accountability
360-degree view
Initial cost
Pros
Cons
Notes: Like it or not, we all have to deal with public risk.
Security is paramount, especially with a single staff operation
Avoids the “he said, she said” scenarios
Today’s systems are merged with back-up cameras and stitch all 4 exterior cameras into a 360 degree view.
Telemetric and driver behavior can also be monitored
Real-time monitoring via ruggedized modem!

## Slide 51: Specifications
Notes: Barbara went over some general considerations. Now it’s time to write some specifications. 

## Slide 52: Specification types
Performance Specifications
  Description of operating requirements (e.g., gross weight, maximum speed, acceleration rate, fuel economy, etc.)
Design Specifications
  Description of physical dimensions (e.g., length, volume carrying capacity, tensile strengths, or other engineering parameters)
Proprietary Specifications
  Description of vehicle’s required equipment (e.g., Caterpillar engine, Allison transmission, Eaton rear axle, etc.)
Bid specs may be primarily of one type or encompass elements of each
Be careful not to restrict specs more than necessary to avoid narrowing choices unintentionally
Be specific, yet flexible!

## Slide 53: Specification resources
Other libraries
  Ideally with similar recent projects
Vendors
  Obviously proprietary
Fleet department
  At least with chassis aspect
  Vested in project
Your consultant
  Temporary expertise to supplement your staff
  Efficient and experienced

## Slide 54: Working with your vendor
Notes: So you’ve gone through all the steps and have awarded the project to a vendor. Your work is not done! 

## Slide 55: Hundreds of details
It’s a team effort
Much like building a custom home
Vendor is expert with materials
You’re the expert on delivery flow
Notes: Dimensions, features, patron flow, finish selections, graphics, etc.

## Slide 56: Doing your part
Make timely decisions
Start graphics development early
Choose materials/colors prior to construction
Request photo updates
Weekly phone call with your representative
On-site inspections
Notes: Don’t delay in getting information to the vendor
Graphics are a very subjective element. Could go quickly, but sometimes takes longer than the build!
Make your finish selections in a timely manner
Request weekly photo updates to monitor progress and/or check for errors
Have a frequent and open dialog weekly to iron out any issues
Conduct on-site visits. There’s nothing like being there!

## Slide 57: Let’s conclude
Build your team
Know your community
Develop your infrastructure
Choose the base vehicle and features
Write your specifications
Work with your vendor

## Slide 58: Thank you!!!
Michael Swendrowski
M: 262.510.1397
E: mswendrowski@vehiclesuccess.com
W: www.vehiclesuccess.com
Barbara Battles
M: 732.567.5211
E: bbattles@sbpl.info
W: www.sbpl.info
Notes: Barbara and I would both like to thank you for your time today, and hope you picked up some great tips and information from our presentation!
Please feel free to use the information on the screen to contact me and/or grab a business card and brochure from the back of the room.
We hope you have/had a great conference and we look forward to any questions you may have.